## Slide 1: Customizing OVS using P4
Muhammad Shahbaz
with Sean Choi, Ben Pfaff, Chaitanya Kodeboyina, Changhoon Kim,
Nick McKeown, Nick Feamster, and Jen Rexford
Notes: Hi all, my name is Muhammad Shahbaz. I am a graduate student at Princeton.
Today, I’m gonna talk about our work on “Customizing Open vSwitch using P4”
It’s a joint work with folks at Princeton, Stanford, VMware, and Barefoot.

## Slide 2: Customizing OVS is Hard!
Protocols
Features
Changes
Adding protocols and features requires
- manual changes throughout the source tree
- maintaining changes across newer versions
e.g., adding a new field required touching 12 files
adding a new action required touching 10 files
Notes: [Click]
Customizing OVS is hard
Every new protocol or feature require changes throughout the OVS source tree
One has to manually apply these changes or maintain them across different versions of OVS

## Slide 3: Customizing OVS is Hard!
Protocols
Features
Manual changes are time-consuming and error prone
Changes applied manually
Notes: Manual changes are time-consuming and can lead to (unknown and undrsired) errors

## Slide 4: Customizing OVS is Hard!
Protocols
Features
What if we describe these changes as programs?
Changes specified as a program
This has many benefits:
a. Rapid addition of new protocols and features
b. Automated testing and debugging
c. Backward compatibility
Notes: What if we describe these changes as programs?
[Click]
This has many benefits:
We can rapidly add new protocols or features as programs
Can perform better automation and testing of the installed features
Can make the task of providing backward compatibility simpler
(one can simply install a program that support the required features)
(no need to carry support for old features in new versions or programs)

## Slide 5
Which language should we use for writing these programs
Notes: But which language should use for writing these programs?

## Slide 6: Should we use P4 ?
It’s an open-source language
Describes different aspects of a packet processor
a. Header and Fields
b. Parser
c. Actions
d. Match-Action Tables
e. Control-Flow
Notes: It’s an open-source language and provides support for describing different aspects of a packet processor e.g.,
The match-action forwarding model of P4 makes is a good candidate for OVS.

## Slide 7: Compiling P4 to ?
There are two main aspects:
1. Efficient mapping from P4 to OVS?
2. Cost of programmability on performance?
Notes: However, when compiling P4 to OVS we have to consider two main things:
Can we efficiently map P4 to OVS?
What’s the cost of programmability on performance?

## Slide 8: A (Magnified) View of Architecture
Fast-Path
Slow-Path
Flow
Extraction
Flow Struct
Cache
Lookup
Match-Action (MA)
Pipeline
Actions
Hit
Miss
ingress
egress
Fast-Path
Slow-Path
Runtime Configurations
Notes: Before looking into these two aspects, let’s us take a look at the magnified view of the OVS architecture.
OVS broadly has two main parts:
Fast-Path
Slow-Path
The packet first arrives at the Fast-Path where the flow extraction function extracts the flow information from the packet. A flow is a parsed representation of the incoming packet.
It’s then looked up in the cache and if there is a miss, it’s sent to the slow-path (Match-Action Pipeline), otherwise, it’s processed by the actions associated with that flow entry.
(3) There is runtime configuration part (made up of ovs command line utilities).
So, in summary, there are potentially 6 main areas, that need to updated when a new change is applied.

## Slide 9: Mapping P4 to ?
Flow Struct
Header, Metadata,
Valids, Stacks, Field Refs
Flow Extraction
Parsed Representation
Match-Action Pipeline
add/remove_header
drop, no_op, add,add_to_field
modify_field
Actions
deparsing, Calculated Fields,
generate_digest
Runtime Configurations
Field Lists,
Action Defs, Table Decls,
Control-Flow
Notes: Field refs become fully qualified names in Flow Struct.

## Slide 10: Mapping P4 to ?
Flow Struct
Header, Metadata,
Valids, Stacks, Field Refs
Flow Extraction
Parsed Representation
Match-Action Pipeline
add/remove_header
drop, no_op, add,add_to_field
modify_field
Actions
deparsing, Calculated Fields,
generate_digest
Runtime Configurations
Field Lists,
Action Defs, Table Decls,
Control-Flow
Notes: Field refs become fully qualified names in Flow Struct.

## Slide 11: Add/Remove Header and Deparsing
P4 provides primitive actions for arbitrarily adding/removing headers to/from packets
a. add_header
b. remove_header
- e.g., for packet encapsulation and decapsulation
Deparser operation serializes the packet
- Its algorithm is inferred from the parse graph
Notes: One of the major difference between P4 processing model and OVS is that P4 provides support for arbitrary header
additions and removals.
It provides primitive actions, like add/remove_header in the MAT pipeline for this purpose
[Click]
A Deparser operations (not explicitly defined in P4 v1.0 spec) serializes the packet before sending it to the egress
Its algorithm is inferred from the parse graph used for flow extraction

## Slide 12: Add/Remove Header and Deparsing
In OVS, changes are applied directly on the packet using set_field() action in the Fast-Path
Actions
Hit
egress
(packet)
(packet)
Fast-Path
[set_field() …]

## Slide 13: Add/Remove Header and Deparsing
Thus, multiple set_field() operations can lead to no change, if header’s valid bit is not set at the time of deparsing
Whereas, in P4, each header has a valid bit
a. If it’s set, changes are written to the packet by the deparser
b. Otherwise, packet is not modified

## Slide 14: Add/Remove Header and Deparsing
This requires keeping a separate copy of each header (or flow) in the Fast-Path
Changes are applied directly to this header
At deparsing stage, if the header is valid it’s written to the packet else it’s discarded
Actions
Hit
egress
(packet, flow)
(packet)
Fast-Path
[set_field(flow) …, deparse]

## Slide 15: Cost of Programmability on Performance?
There are three main factors that primarily affect the performance:
1. Packet Parsing
2. Packet Deparsing
3. Fast-Path Actions
Notes: There are three main factors that affect the performance of OVS when compiled via P4.

## Slide 16
Notes: To quantify the affect we did some preliminary evaluations using the following setup.
It’s an Open vSwitch v 2.4.90.

## Slide 17: Cost of Programmability on Performance?
a. Layer2 learning switch
Chart: Packet Size (Bytes)
| 64.0 | 68.0 | 72.0 | 128.0 | 536.0 | 1514.0
Vanilla OvS | 9999.5 | 9999 | 9999.5 | 9989 | 10000 | 10000
P4 OvS (-O0) | 9396.5 | 9782 | 9900.5 | 10000 | 10000 | 10000
b. Layer3 simple router
Chart: Packet Size (Bytes)
| 64.0 | 128.0 | 256.0 | 536.0 | 1514.0
Vanilla | 8099 | 9815.5 | 9902 | 10000 | 10000
P4 (-O0) | 1970.5 | 3437 | 6406.5 | 10000 | 10000
P4 OVS (-O0): no csum | 2734 | 4760 | 8870 | 10000 | 10000
Notes: Here we show performance plots for two P4 programs
l2_switch.p4
simple_router.p4
What we have seen is that packet parsing/deparsing are the primary bottlenecks in this case.
Performance degrades with increasing no. of protocols
e.g., 19% decrease in Vanilla OvS with IP protocol parsing
This is more significant in P4 OvS as fast-path maintains its own copy of the parsed representation (i.e., extra overhead on parsing)
The P4-OVS plots show results for unoptimized compilation. However, with careful analysis we can avoid these extra copies in the fast-path.
For example, in case l2_switch.p4 we know for a fact that we are not adding or removing any headers (or even setting any field). Thus, the
compiler can use this information to avoid extra header copies in the fast-path in the final code.

## Slide 18: Future Work
  Implement optimizations to avoid extra copies of the header (or flow) in the fast-path
  - using dead-code elimination and liveness analysis etc.
  Provide support for general fast-path actions like add_to_field etc.
Notes: Currently, we are working on building optimizations to avoid keeping extra copies of these headers in the fast-path.
We are looking into traditional compiler optimizations like dead-code elimination and liveness analysis to see if we can leverage them in our case.

## Slide 19: Questions?
Source Code
https://goo.gl/jlRHih
Muhammad Shahbaz
mshahbaz@cs.princeton.edu
Notes: With this I conclude my presentation. Thank you, and I’m happy to take any questions.